## Slide 1: VHC010-VHC011 The mini-industrial vacuums range compressed air drive

## Slide 2: Agenda
Mini IVS range and layouts
Jobs to be done
Key features and benefits
Accessories
1
2
3
4
Marketing material
Technical specification
Naming and hierarchy
The corporate responsibility
5
6
7
8

## Slide 3: 1
Mini IVS compressed air layouts

## Slide 4: VHC010 / VHC011 Z1
Compressed air driven industrial vacuum cleaner
An industrial vacuum powered by compressed air is a device used for cleaning and maintaining industrial environments. It operates by using a high-speed air stream, generated through an air compressor, to create powerful suction that collects dust, debris, liquids, and other materials.
Main applications
Compressed air is often preferred in environments where electricity could pose a risk or where it's necessary to handle flammable or combustible materials, as the use of compressed air eliminates the risk of electrical sparks. They are utilised in a variety of industries, including, electronic, pharmaceutical, additive manufacturing, and chemical industry, to keep workplaces clean and improve safety and operational efficiency.
Compressed air industrial vacuum cleaner

## Slide 5: Mini IVS
Range introduction
Introduction
Mini-IVS is a platform of industrial vacuum cleaner of small and compact footprint. The range is designed for industrial application as alternative solution to the 400 mm platform, bigger machine VHC110 and VHC120, always compressed air driven.
Designed for dry collection of powders and fine powders or grains, combustible and or conductive and hazardous dusts.
Range key feature:
One layout with safe disposal – body 010
One layout with pull clean filter cleaning system without needs of consumable – body 011
Lightweight and robust, perfect solution for fast and frequent cleaning job also in narrow spaces or when the are obstacles on the floors or difficult places to reach
New dedicated range of industrial reduced footprint accessories, EXA
MEET NILFISK’S MINI INDUSTRIAL VACUUMS
Small but mighty
Maximum performance, safety, and flexibility. Minimum footprint.

## Slide 6: Mini IVS
Layout
Safe disposal – body 010
Container 30 L
Configuration: bag filter + safety filter H14
Suitable for combustible dust and ATEX
Suitable for hazardous dusts
Pull&Clean – body 011
Container 15 L with removable wheel-base
Optional Upstream HEPA14 filter (US included)
Suitable for combustible dust and ATEX
Suitable for hazardous dust
Pump enclosure
Body 011
Body 010
VHC011 Z1 EXA
VHC010 SBS Z1 EXA

## Slide 7: Product definition: compressed air architecture
Section view: flow schematic and architecture Z1/EXP models
VHC010 Z1 EXA
Safe disposal with:
Class M antistatic fleece filter
Process air
Always 3 filtration stage
VHC011 Z1 EXA
With conical cartridge Class M and Pull&Clean™
*ULPA for stainless steel versions
VHC010 Z1 EXA SBS
Safe disposal with:
Safe bag system: SBS
VHC010 Z1 EXA DBS
Safe disposal with:
Class M antistatic fleece filter + guillotine valve
Cleaned Process air
UP to 3 filtration stage
MCLASS bag filter
H14 HEPA
E10
E10
MCLASS cartridge
H14 HEPA
E10
E10

## Slide 8: 2
Jobs to be done

## Slide 9: Focus segments and jobs to be done
AM industry
Production line, part of the process
Typical cleaning job:
  Collection and cleaning metal 3D printers, glove box, finished parts, emptying bins…
Key features:
  Certified for conductive combustible dust, safe with IP65 enclosure
  Safe bag system disposal
  Downstream ULPA filters option available
Chemical Industry
Laboratories and production
Typical cleaning job:
  Collecting powders in environments with solvents, test batches…
  Cleaning of floors, desks, surfaces
Key features:
  For Z1 Atex zones and for combustible dusts
  Long life filter and no consumables
  Washable container
  Downstream ULPA filters option available
Electronic
PCB production, components production
Typical cleaning job:
  Cleaning of work benches and working areas using existing pneumatic lines
  Cleaning of floors, and surfaces
Key features:
  No electrical parts
  Easy to connect to existing pneumatic distribution
  Avoid spark generation
Pharma
Primary and secondary packaging
Typical cleaning job:
  Cleaning pharmaceutical process machines or process equipment
  Cleaning laboratories equipment in Z1 areas
Key features:
  Fully Stainless-steel body
  HEPA14 filtration
  Not contaminating working environment
  Downstream ULPA filters option available

## Slide 10: 3
Key features and benefits

## Slide 11: Key features and design
VHS011 Z22 EXA / C2D2
Vacuum gauge for a constant monitoring of the performance and filtration efficiency
PullClean cleaning filter system, easy and efficient operation
High efficiency filters: M-Class (as standard); PTFE or HEPA 14 upstream filter 99,995% 0.1-0.2 microns (as option) all filters are antistatic
Safe and mistake proof connection for certified ATEX accessories Ø40 EXA
15 L removable container AISI304, easily washable thanks to removable wheel-base
Antistatic wheels
Rounded shape for an easy cleaning of the overall surface
Quiet – only 70 dB(A) level noise
Easy and fast service: everything quickly accessible
Fully grounded and bonded, avoids electrostatic sparks, electrical hazard
Parking brake, stable also on slightly sloped
High manoeuvrable thanks to the 4 ball bearing pivoting wheels
Protection bracket
Optional pressure regulator
Air manual valve
Free dust pump enclosure with optional downstream ULPA filter
Air supply
Grounding clamp
Handle with grounding cable holder
Accessories holder

## Slide 12: Key features and design
VHC010 Z1 / CID1
Protection bracket
Optional pressure regulator kit
Air manual valve
HEPA 14 safety filter efficiency 99,995% 0.1-0.2 microns
30 L externally painted AISI 304 container
Safe and mistake proof connection for certified ATEX EXA accessories Ø40
Fully grounded and bonded, avoids electrostatic sparks, electrical hazard
Rounded shape for an easy cleaning of the overall surface
Quiet – only 70 dB(A) level noise
Convenient and safe disposal system
Parking brake, stable also on slightly sloped
High manoeuvrable, container with 4 ball bearing pivoting wheels
Antistatic wheels
Air supply
Grounding clamp
Handle with grounding cable holder
Accessories holder
Vacuum gauge for a constant monitoring of the performance and filtration efficiency
Free dust pump enclosure with optional downstream ULPA filter

## Slide 13: PullClean
Description
Pull clean filter cleaning system is a manual system with which operator can easily clean the filter and keep high the efficiency of the vacuum cleaner
How it works
The cleaning of the filter is done with the inlet of the machine closed
Three rapid opening and closing of the blue flap create a counter impulsive flow into the filter that is in this way cleaned
Rapidly repeat the cleaning process for three times for the perfect cleaning of the filter
Value and benefit
Reduced maintenance
Stable performance make faster the cleaning job
Safe method of clean the filter without stop the suction
VHC011 Z1 EXA
Efficient filter cleaning

## Slide 14: Safe bag system
Description
SBS models are quipped with the safe bag system; this disposal system allow to dispose the collected material without being in contact with the material itself
How it works
It is built with a CLASS M fleece filter and a special bag inlet with safety guillotine valve, externally protected by a conductive and resistant plastic bag
The bag filter safely collect the material, external plastic bag protects operator from the contact with the filtering bag during the disposal procedure
The guillotine valve, when manually closed, avoid any leakage of dust from the inlet of the safe bag system
Value and benefit
Perfect protection accordingly different types of hazardous dusts
Secondary protection with HEPA14 certified filter
Safe, easy and quick disposal system
VHC010 Z1 EXA SBS
No dust exposure

## Slide 15: 4
Accessories and optionals

## Slide 16: Mini IVS VHC010 Z1 & VHC011 Z1
EXA Ø40 mm accessories (also for IECEX and CID1)
EXA connection with PIN
EXA antistatic hose 3 m FDA,
EXA bent connection AISI 304
EXA conductive cone black
EXA flat lance AISI 304 300 mm NEW
EXA conductive nozzle Ø40-32
EXA antistatic hose 3 m,
EXA bent connection AISI 304
EXA AISI 304 antistatic cone
EXA AISI 304 flat lance 300 mm NEW
EXA AISI 304 antistatic round brush
EXA small handgrip (for bent connection) NEW
EXA AISI 304 mobile floor nozzle 300 mm NEW
EXA antistatic hose 3 m polyurethan FDA
EXA bent connection AISI 304
EXA antistatic cone silicon transparent
EXA flat lance AISI 304 300 mm NEW
EXA silicon nozzle with D40-32 reduction
EXA antistatic hose 3 m
EXA bent connection
EXA conductive cone
Basic Ø40 mm EXA (available also in combo version: CB)
4072400773
Machineries FDA Ø40 mm EXA
(complete) Ø40 mm
4072400822
General cleaning Ø40 mm EXA
4072400824
Machineries conductive Ø40 mm EXA (complete) Ø40 mm
4072400823
1
3
2
1
2
3
4
5
1
3
5
2
4
2
3
4
6
7
5
1

## Slide 17: Mini IVS VHC010 & VHC011 combustible dust
ACD Ø40 mm accessories kits
ACD sleeve connection
Antistatic FDA transparent hose 3 m + sleeves,
AISI 304 bent connection
Silicone Antistatic FDA Cone
Flat lance AISI 300 mm NEW
Reducer Ø40/Ø32 SS
Flexible nozzle autoclavable Ø32
Flex conductive hose 3 m + sleeves
AISI304 bent connection
Conductive cone
AISI 304 flat lance 300 mm NEW
Antistatic floor nozzle 300 mm NEW
AISI 304 small handgrip 2 parts NEW
Round antistatic brush
Flex conductive hose 3 m + sleeves
AISI304 bent connection
Conductive cone
Basic ANTIST. Kit ACD Ø40
4072400825
General kit ACD Ø40
4072400774
Machineries FDA ACD kit Ø40
4072400826
1
2
3
1
2
3
4
5
6
7
1
2
3
6
5
4

## Slide 18: Accessory holder
Description
Four convenient and robust clips, two each side, useful to easily transport up to 4 end tools
How it works
When IVAC is parked, the accessories holder can easily keep the new small handgrip and floor nozzle
Disconnect hose from IVAC’s inlet and handgrip for an easiest positioning
Disconnect bulky accessories, as handgrip and floor nozzle, before moving the machines
Value and benefit
Accessories always nearby
Parking with minimum space occupation
Electric version represented
Parking position

## Slide 19: Product definition
Description
Optional pressure regulator kit can be easily installed using the screws of the accessory holder
How it works
Set the proper supply pressure reducing to the desired value (5-6 bar)
It grants always the maximum performance by taking under control the pressure loss of the supply line
It is suggested when IVAC is connected far from the main pneumatic supply line
Value and benefit
It is small, compact and easy to install
It is ergonomic and well protected
It assures always the best performance
New pressure regulator kit
Pressure regulator kit

## Slide 20: VHC010 Z1 EXA filters
Spare filter and bags filters for VHC010...
HEPA14 spare filter: 4081701910 (only filter)
5 PC fleece filter: 107419592 (standard models)
5 PC fleece filter + guillotine valve 4089101208 (standard models only)
5 PC safe bag system: 4089101209 (SBS models only)
* Refer to user manual and spare part list for maintenance and spare kits
HEPA H14
4081701910
All versions of VHS010
Standard
107419592
VHC010 Z1
5PC
Dust Bag System
4089101208
VHC010 Z1 DBS
5PC
Safe Bag System
4089101209
VHC010 Z1 SBS
5PC

## Slide 21: VHC011 Z1 EXA filters
HEPA H14
4081701910
Included in VHC011 AU versions
Standard
4081701855*
VHC011
VHS011 LC Z22 EXA / C2D2 and VHS011 LC ACD
HEPA14 spare filter: 4081701910
Primary Filter Cat. M: 4081701855
Primary Filter Cat. M PTFE: 4081701856
* Refer to user manual and spare part list for maintenance and spare kits

## Slide 22: 5
Marketing material

## Slide 23: VHC010/011 – Dealer Package
Brochure
Factsheet
Instructions for Use
Location Images
Main Data File
Sales Presentation
Spare Parts
Renders
Dealer package
You can find the Dealer Package on the
Dealer Portal

## Slide 24: 6
Technical specification

## Slide 25: Technical data EU-UK
Mini IVS compressed
Technical data | Unit | VHC010 Z1 EXA | VHC010 Z1 EXA SBS | VHC010 Z1 EXA 2X SBS | VHC011 Z1 EXA | VHC011 Z1 EXA AU | VHC011 Z1 EXA 3X
PN |  | 4061300042 | 4061300043 | 4061300044 | 4061300045 | 4061300046 | 4061300047
Air consumption | NL/min | 630 | 630 | 630 | 630 | 630 | 630
Feeding pressure | Bar | 6 | 6 | 6 | 6 | 6 | 6
Max airflow | L/min – m³/h | 2033 - 122 | 2033 - 122 | 2033 - 122 | 2033 - 122 | 2033 - 122 | 2033 - 122
Airflow with 3-meter hose | L/min – m³/h | 110 | 110 | 110 | 110 | 110 | 110
Vacuum max | kPa – mbar | 34 - 340 | 34 - 340 | 34 - 340 | 34 - 340 | 34 - 340 | 34 - 340
Ø Air supply hose external-internal | Mm | 12-10 | 12-10 | 12-10 | 12-10 | 12-10 | 12-10
Sound pressure level | dB(A) | 70 | 70 | 70 | 70 | 70 | 70
Container capacity | L | 30 | 30 | 30 | 15 | 15 | 15
Main filter type |  | Fleece M class | SBS | SBS | Cartridge M CLASS | Cartridge M CLASS | Cartridge M CLASS
Main filter area | cm² | – | – | – | 9000 | 9000 | 9000
Upstream HEPA filter H14 area | cm² | 12000 | 12000 | 12000 | – | 12000 | –
Inlet | mm | EXA 40 | EXA 40 | EXA 40 | EXA 40 | EXA 40 | EXA 40
Length x Width x Height | cm | 41x43x83 | 41x43x83 | 41x43x83 | 41x43x83 | 41x43x83 | 41x43x83
Weight | kg | 17 | 17 | 17 | 19 | 19 | 19

## Slide 26: Technical data US
Mini IVS compressed
Technical data | Unit | VHC010 EXP SBS | VHC010 EXP 2X SBS | VHC011 EXP AU | VHC011 EXP AU 3X
PN |  | 4061300048 | 4061300049 | 4061300050 | 4061300051
Air consumption | NL/min | 630 | 630 | 630 | 630
Feeding pressure | Bar | 6 | 6 | 6 | 6
Max airflow | L/min – m³/h | 2033 - 122 | 2033 - 122 | 2033 - 122 | 2033 – 122
Airflow with 3-meter hose | L/min – m³/h | 110 | 110 | 110 | 110
Vacuum max | kPa – mbar | 34 - 340 | 34 - 340 | 34 - 340 | 34 – 340
Ø Air supply hose external-internal | Mm | 12-10 | 12-10 | 12-10 | 12-10
Sound pressure level | dB(A) | 70 | 70 | 70 | 70
Container capacity | L | 30 | 30 | 15 | 15
Main filter type |  | SBS | SBS | Cartridge M CLASS | Cartridge M CLASS
Main filter area | cm² | – | – | 9000. | 9000
Upstream HEPA filter H14 area | cm² | 12000 | 12000 | 12000 | 12000
Inlet | mm | EXA 40 | EXA 40 | EXA 40 | EXA 40
Length x Width x Height | cm | 41x43x83 | 41x43x83 | 41x43x83 | 41x43x83
Weight | kg | 17 | 17 | 19 | 19

## Slide 27: 7
Naming and product hierarchy

## Slide 28: Naming and product hierarchy
C:
compressed air driven
VHC010 SBS Z1 EXA
0: 320 mm platform
0: Safe disposal
VHC011 Z1 EXA
0: 320 mm platform
1: Pull&Clean version
Acronyms
Acronyms
C:
compressed air driven
1: Pneumatic pump
1: Pneumatic pump
L3 = Compressed air
L4 = VHC01 ATEX
L5 = VHC010 ATEX
L6: • VHC010 Z1 EXA
• VHC010 SBS Z1 EXA
L5 = VHC011 ATEX
L6: • VHC011 Z1 EXA
• VHC011 Z1 EXA AU
L5 = VHC010 EXP
L6: • VHC010 EXP
• VHC010 SBS EXP
L5 = VHC011 EXP
L6: • VHC011 EXP
• VHC011 EXP AU
* Non HazLoc/Atex model upon request
*L4 = VHC01
L5 = VHC010
L6: • VHC010 CD
• VHC010 CD SBS
L5 = VHC011
L6: • VHC011 CD
• VHC011 CD AU

## Slide 29: PNs and versions available at launch date
Model type | PN | 
4061300042 | VHC010 Z1 EXA | EU
4061300043 | VHC010 Z1 EXA SBS | 
4061300044 | VHC010 Z1 EXA 2X SBS | 
4061300045 | VHC011 Z1 EXA | 
4061300046 | VHC011 Z1 EXA AU | 
4061300047 | VHC011 Z1 EXA 3X | 
4061300048 | VHC010 EXP SBS | US
4061300049 | VHC010 EXP 2X SBS | 
4061300050 | VHC011 EXP AU | 
4061300051 | VHC011 EXP AU 3X | 

## Slide 30: 8
The corporate responsibility

## Slide 31: The corporate responsibility
No emissions during production
Recyclable metal and parts
All the parts (except for the filters) are made of recyclable materials